## Slide 1: Rendering Pipeline
Each stage can be also pipelined
The slowest of the pipeline stage determines the rendering speed.
Frames per second (fps)
Rasterizer
Geometry
Application
CPU

## Slide 2: Application Stage
Executes on the CPU
Collision detection – may provide the feedback
Global acceleration algorithms, etc
Generate rendering primitives, points, lines, triangles ..
Input from other sources (keyboard, mouse..)
..

## Slide 3: Geometry stage
The majority of the per-polygon and per-vertex operations (Floating point operations)
Intel’s MMX/SSE
Old time: Software implementation.
Move objects (matrix multiplication)
Move the camera (matrix multiplication)
Compute lighting at vertices of triangle
Project onto screen (3D to 2D)
Clipping (avoid triangles outside screen)
Map to window

## Slide 4: Geometry stage
Move objects (matrix multiplication)
Move the camera (matrix multiplication)
Compute lighting at vertices of triangle
Project onto screen (3D to 2D)
Clipping (avoid triangles outside screen)
Map to window
Model & View
Transform
Vertex
Shading
Projection
Clipping
Screen
Mapping

## Slide 5: What’s a Vertex?
The defining “corners” of a primitive
Often means a triangle
A
Triangle
Vertices
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007 ECE 498AL, UIUC

## Slide 6: The RASTERIZER stage
From GEOMETRY to visible pixels on screen
Add textures and various other per-pixel operations
And visibility is resolved here: sorts the primitives in the z-direction
Per pixel operation
Mostly integer operations

## Slide 7
Rasterizer
Geometry
Application
Frame Buffer

## Slide 8: Color Framebuffer
2D array of R,G,B color pixel values
8 bits (256 levels) per color component
Three 8-bit components can represent 16 million different colors, including 256 shades of gray
4th component: alpha; used for blending
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007 ECE 498AL, UIUC

## Slide 9: Interfaces between CPU and GPU
AGP: Advanced Graphics Port – an interface between the computer core logic and the graphics processor
  AGP 1x: 266 MB/sec – twice as fast as PCI
  AGP 2x: 533 MB/sec
  AGP 4x: 1 GB/sec  AGP 8x: 2 GB/sec
  256 MB/sec readback from graphics to system
PCI-E: PCI Express – a faster interface between the computer core logic and the graphics processor
  PCI-E 1.0: 4 GB/sec each way  8 GB/sec total
  PCI-E 2.0: 8 GB/sec each way  16 GB/sec total
AGP
http://www.cis.upenn.edu/~suvenkat/700/

## Slide 10: Generation I: 3dfx Voodoo (1996)
http://accelenation.com/?ac.id.123.2
One of the first true 3D game cards
Worked by supplementing standard 2D video card.
Did not do vertex transformations: these were done in the CPU
Did do texture mapping, z-buffering.
Primitive
Assembly
Vertex
Transforms
Frame
Buffer
Raster
Operations
Rasterization
and
Interpolation
CPU
GPU
PCI

## Slide 11: Generation II: GeForce/Radeon 7500 (1998)
Vertex
Transforms
http://accelenation.com/?ac.id.123.5
Main innovation: shifting the transformation and lighting calculations to the GPU
Allowed multi-texturing: giving bump maps, light maps, and others..
Faster AGP bus instead of PCI
Primitive
Assembly
Frame
Buffer
Raster
Operations
Rasterization
and
Interpolation
GPU
AGP

## Slide 12: Generation III: GeForce3/Radeon 8500(2001)
Vertex
Transforms
http://accelenation.com/?ac.id.123.7
For the first time, allowed limited amount of programmability in the vertex pipeline
Also allowed volume texturing and multi-sampling (for antialiasing)
Primitive
Assembly
Frame
Buffer
Raster
Operations
Rasterization
and
Interpolation
GPU
AGP
Small vertex
shaders

## Slide 13: Generation IV: Radeon 9700/GeForce FX (2002)
Vertex
Transforms
http://accelenation.com/?ac.id.123.8
This generation is the first generation of fully-programmable graphics cards
Different versions have different resource limits on fragment/vertex programs
Primitive
Assembly
Frame
Buffer
Raster
Operations
Rasterization
and
Interpolation
AGP
Programmable
Vertex shader
Programmable
Fragment
Processor

## Slide 14: Generation IV.V: GeForce6/X800 (2004)
Not exactly a quantum leap, but…
Simultaneous rendering to multiple buffers
True conditionals and loops
Higher precision throughput in the pipeline (64 bits end-to-end, compared to 32 bits earlier.)
PCIe bus
More memory/program length/texture accesses

## Slide 15
Vertex
Index
Stream
3D API
Commands
Assembled
Primitives
Pixel
Updates
Pixel
Location
Stream
Programmable
Fragment
Processor
Transformed
Vertices
Programmable
Vertex
Processor
GPU
Front End
Primitive
Assembly
Frame
Buffer
Raster
Operations
Rasterization
and
Interpolation
3D API:
OpenGL or
Direct3D
3D
Application
Or Game
Pre-transformed
Vertices
Pre-transformed
Fragments
Transformed
Fragments
GPU
Command &
Data Stream
CPU-GPU Boundary (AGP/PCIe)
Fixed-function pipeline

## Slide 16: NVIDIA GeForce 7800 Pipeline

## Slide 17: GeForce 8800
16 highly threaded SM’s, >128 FPU’s, 367 GFLOPS, 768 MB DRAM, 86.4 GB/S Mem BW, 4GB/S BW to CPU
Load/store
Global Memory
Thread Execution Manager
Input Assembler
Host
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Load/store
Load/store
Load/store
Load/store
Load/store
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007 ECE 498AL, UIUC

## Slide 18
Xbox 360 : Unified shader (ATI/AMD)
Playstation 3: a modified version of GeForce 7800 (NVIDIA)
Cuda: unified shader (NVIDIA)

## Slide 19: The GEOMETRY stage in more detail
The model transform
Originally, an object is in ”model space”
Move, orient, and transform geometrical objects into ”world space”
Example, a sphere is defined with origin at (0,0,0) with radius 1
  Translate, rotate, scale to make it appear elsewhere
Done per vertex with a 4x4 matrix multiplication!
The user can apply different matrices over time to animate objects

## Slide 20: The view transform
You can move the camera in the same manner
But apply inverse transform to objects, so that camera looks down negative z-axis
z
x

## Slide 21: GEOMETRY Lighting
Compute ”lighting” at vertices
light
Geometry
blue
red
green
Try to mimic how light in nature behaves
  Empirical models and some real theory
Rastrizer
(interpolation)

## Slide 22: GEOMETRY Projection
Two major ways to do it
  Orthogonal (useful in few applications)
  Perspective (most often used)
    Mimics how humans perceive the world, i.e., objects’ apparent size decreases with distance
Application
Geometry
Rasterizer

## Slide 23: GEOMETRY Clipping and Screen Mapping
Square (cube) after projection
Clip primitives to square
Screen mapping, scales and translates square so that it ends up in a rendering window
These ”screen space coordinates” together with Z (depth) are sent to the rasterizer stage

## Slide 24: GEOMETRY Summary
model space
world space
world space
compute lighting
camera space
projection
image space
clip
map to screen

## Slide 25: The RASTERIZER in more detail
Scan-conversion
  Find out which pixels are inside the primitive
Texturing
  Put images on triangles
Interpolation over triangle
Z-buffering
  Make sure that what is visible from the camera really is displayed
Double buffering
And more…

## Slide 26: The RASTERIZER Scan conversion (Traingle traversal)
Triangle vertices from GEOMETRY is input
Find pixels inside the triangle
  Or on a line, or on a point
Do per-pixel operations on these pixels:
  Interpolation
  Texturing
  Z-buffering
  And more…

## Slide 27: The RASTERIZER Interpolation
Interpolate colors over the triangle
  Called Gouraud interpolation
blue
red
green

## Slide 28: The RASTERIZER Texturing
+
=
One application of texturing is to ”glue” images onto geometrical object
  Associate points in an image to points in a geometric object

## Slide 29: Examples
From wikipedia
Without texture mapping
With texture mapping

## Slide 30: Another Example: Bump mapping
From wikipedia
+
=

## Slide 31: The RASTERIZER Z-buffering
The fixed graphics hardware ”just” draws triangles
However, a triangle that is covered by a more closely located triangle should not be visible
Assume two equally large tris at different depths
Triangle 1
Triangle 2
Draw 1 then 2
incorrect
Draw 2 then 1
correct

## Slide 32: The RASTERIZER Z-buffering
Would be nice to avoid sorting…
The Z-buffer (aka depth buffer) solves this
Idea:
  Store z (depth) at each pixel
  When scan-converting a triangle, compute z at each pixel on triangle
  Compare triangle’s z to Z-buffer z-value
  If triangle’s z is smaller, then replace Z-buffer and color buffer
  Else do nothing
Can render in any order

## Slide 33: The RASTERIZER Double buffering
The monitor displays one image at a time
So if we render the next image to screen, then rendered primitives pop up
And even worse, we often clear the screen before generating a new image
A better solution is ”double buffering”

## Slide 34: The RASTERIZER Double buffering
Use two buffers: one front and one back
The front buffer is displayed
The back buffer is rendered to
When new image has been created in back buffer, swap front and back

## Slide 35: 3D pipeline
Rasterizer
Geometry
Application
Frame Buffer

## Slide 36: Graphics Processor Trend
Fixed pipeline processor
  More and more CISC style processors
  OpenGL API~= One instruction
Programmable parallel processors
  Scatter/Gather operations
  Scatter: Aout[B[i]]=Ain[i]
  Gather: Aout[i]=Ain[B[in]]
  Enable GPGPU

## Slide 37: Fixed Function vs. Programmable Function
Fixed function stage:
  Fixed vertex stage: Cilp-space vertex computations, per-vertex normal, many other per-vertex operations (color material, texture coordinate, normal transformation)
  Fixed fragment stage: many basic lighting models and effects etc.
Programmable function pipeline
  Custom computations

## Slide 38: OpenGL pipeline(1997)

## Slide 39: OpenGL 3

## Slide 40: Fixed Function Scheme

## Slide 41: Programmable Function Scheme

## Slide 42: Hardware Design Issues in Fixed Pipeline
Start from straightforward mapping
Efficient Instruction mapping
  Better compiler is good
Primitive Assembly
Efficient Rasterization
Register Bank issues
Texture cache access
  Prefetching
Memory bandwidth
Better optimizations to reduce the amount of computations,

## Slide 43: OpenGL Rendering Pipeline
http://glprogramming.com/red/

## Slide 44: View Transformation

## Slide 45: GEOMETRY Summary (Review)
model space
world space
world space
compute lighting
camera space
projection
image space
clip
map to screen

## Slide 46: Vertex & Primitives
V1
V2
V3
V1 = (x1, y1, z1)
V2 = (x2, y2, z2)
V3 = (x3, y3, z3)
+x
+y
+z
Normal vectors:
Surface Normals: Physical meaning
Vertex Normals: Useful for fast and effective lighting algorithms

## Slide 47: Primitive Assembly

## Slide 48
Model Space: Each model has own coordinate
Word Space: All models have the same coordinate
Camera Space (Eye Space): Relative to the camera (eye) position. (Camera position, z = 0)
Screen space: Actual hardware coordinates

## Slide 49: Transformation Pipeline
World Transformation
  Model coordinates  World coordinates
View Transformation
  World coordinates  Camera Space
Projection Transformation
  Camera Space  View Plane
Matrix Multiplications for transformations
From Hsien-Hsin Lee’s MPG class

## Slide 50: Homogeneous Coordinates
Adding one more imaginary coordinate
Enable all transformations to be done by “multiplication”
“projective transformations” can be easily represented
Add one coordinate (w) to 3D vector
  W=1 is a cartesian coordinate
  W >1 useful for projective projection

## Slide 51: Transformations
+x
+y
+z
(tx, ty, tz)
+x
+y
+z
(x1’, y1’, z1’)
(x1, y1, z1)
x1’
y1’ =
z1’
[
x1 tx
Y1 + ty
z1 tz
]
[
]
x1’ 1 0 0 tx
y1’ = 0 1 0 ty
z1’ 0 0 1 tx
1 0 0 0 1
]
[
x1
y1
z1
1
[
]

## Slide 52: Others
Scaling
Rotation (with Z-axis)
x1’ Sx 0 0 0
y1’ = 0 Sy 0 0
z1’ 0 0 Sz 0
1 0 0 0 1
]
[
x1
y1
z1
1
[
]
x1’ cosΘ sinθ 0 0
y1’ = -sinθ cosθ 0 0
z1’ 0 0 1 0
1 0 0 0 1
]
[
[
]
x1
y1
z1
1

## Slide 53: Non-commutative Property
[X’] = [A][B][X] ≠ [B][A][X]
+z
+z
Scale by 2
X,Y translate +5, +5
+z
X,Y translate +5, +5
Scale by 2
(1,1,-1)

## Slide 54: Affine Transformation
Line  Line
  keep straight lines, ratios of distances between points
Angle can be changed

## Slide 55: Projects
Orthographic projection
Projective projection

## Slide 56: Canonical View Volume
Orthographic Project
OpenGL GL_Projection matrix
+z
+x
+y
+z
+x
+y

## Slide 57: Field of View
d
ys
y
z
Frustrum: the region of space in the modeled world that may appear on the screen
near
far

## Slide 58: Prospective Projection
near
far
+z
+x
+y

## Slide 59: Data Structures in Pipeline
Vertex assembly
Primitive assembly
Rasterization
Fragment operations
Display
Vertex operations
Application
Primitive operations
struct { float x,y,z,w; float r,g,b,a; } vertex;
struct { vertex v0,v1,v2 } triangle;
struct { short int x,y; float depth; float r,g,b,a; } fragment;
struct { int depth; byte r,g,b,a; } pixel;
Frame buffer
Screen coordinates
Akeley Fall 2007 Slides
Not in this project
Not in this project

## Slide 60: Graphics Pipeline
Design option #1
  Expand Execution stage to include graphics functional units
Design option #2
  Add additional pipeline stages after the WB stage
Need triangle setup unit
Need a separate stage for Rasterizer

## Slide 61: Graphics Instructions

## Slide 62: Registers
Vector Registers (64bits = 16bits * 4)
  There are 64 vector registers.
  Each vector register holds 4 elements (Scalar Registers).
  All vectors store only floating-point numbers.
  Use idx field to indicate an element.
Vector Register |  |  | 
elmt 3 | elmt 2 | elmt 1 | elmt 0

## Slide 63: VADD instruction
Assembly Formats
  vadd dest src1 src2
Encoded to
Operation
  dest[0] <- src1[0] + src2[0]
  dest[1] <- src1[1] + src2[1]
  dest[2] <- src1[2] + src2[2]
  dest[3] <- src1[3] + src2[3]
Examples
  vadd v0 v1 v2
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  |  | dest |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  | src1 |  |  |  |  |  |  |  | src2 |  |  |  |  | 

## Slide 64: VMOV instruction
Assembly Formats
  vmov dest src
Encoded to
Operation
  dest <- src
Description
  Move Instruction for Vector Registers
Examples
  vmov v1 v2
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  |  | dest |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  | src |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 65: VMOVI instruction
Assembly Formats
  vmovi dest imm16
Encoded to
Operation
  dest[0], dest[1], dest[2], dest[3] <- imm16
Description
  Move Instruction for Vector Registers (Floating-point).
  imm16 will be copied to all four elements of the dest vector register
Examples
  vmovi v1 1000.f
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 |  |  | dest |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
imm16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 66: VCOMPMOV instruction
Assembly Formats
  vcompmov dest idx src
Encoded to
Operation
  dest[idx] <- src
  Note: dest - vector register, src - scalar register
Description
  Move Instruction for Vector Register’s element.
Examples
  vcompmov v1 0 r1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | idx |  | dest |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | src |  |  |  |  |  |  |  |  |  |  | 

## Slide 67: VCOMPMOVI instruction
Assembly Formats
  vcompmovi dest idx imm16
Encoded to
Operation
  dest[idx] <- imm16
Description
  Move Instruction for Vector Register’s element (Floating-point).
Examples
  vcompmovi v1 0 1.5f
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | idx |  | dest |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
imm16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 68: SETVERTEX instruction
Assembly Formats
  setvertex vr
Encoded to
Operation
  The value of vr[1]: X coordinate
  The value of vr[2]: Y coordinate
  The value of vr[3]: Z coordinate
  Ignore the value of vr[0]
Description
  Set the current vertex using vr register
Examples
  setvertex v1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 |  |  | vr |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 69: SETCOLOR instruction
Assembly Formats
  setcolor vr
Encoded to
Operation
  The value of vr[0]: R component
  The value of vr[1]: G component
  The value of vr[2]: B component
  Ignore the value of vr[3]
Description
  Set the color of the current vertex using vr register
Examples
  setcolor v1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |  |  | vr |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 70: ROTATE instruction
Assembly Formats
  rotate vr
Encoded to
Operation
  The value of vr[0]: Angle
  The value of vr[3]: Z-coordinate
  Ignore the value of vr[1] & vr[2]
Description
  Rotate the current matrix using vr register
Examples
  rotate v1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 |  |  | vr |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 71: TRANSLATE instruction
Assembly Formats
  translate vr
Encoded to
Operation
  The value of vr[1]: distance to move on x-axis
  The value of vr[2]: distance to move on y-axis
  Ignore the values of vr[0] & vr[3]
Description
  Translate the current matrix using vr register
Examples
  translate vr1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 |  |  | vr |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 72: SCALE instruction
Assembly Formats
  scale vr
Encoded to
Operation
  The value of vr[1]: scale value on x-axis
  The value of vr[2]: scale value on y-axis
  Ignore the values of vr[0] & vr[3]
Description
  Scale the current matrix using vr register
Examples
  scale v1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |  |  | vr |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 73: PUSHMATRIX instruction
Assembly Formats
  pushmatrix
Encoded to
Operation
Description
  Push the current matrix into the stack.
Examples
  pushmatrix
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 74: POPMATRIX instruction
Assembly Formats
  popmatrix
Encoded to
Operation
Description
  Pop a matrix from the stack to the current matrix.
Examples
  popmatrix
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 75: BEGINPRIMITIVE instruction
Assembly Formats
  beginprimitive type
Encoded to
Pre-defined Types
  Points: 0, Lines: 1, Line strip: 2, Line loop: 3, Triangles: 4, Triangle strip: 5, Triangle fan: 6, Quads: 7, Quad strip: 8, Polygon: 9
  Refer to http://www.jmp.com/support/help/Graphics_Primitives.shtml
Description
  Delimit the vertices that define a primitive or a group of primitives.
Examples
  beginprimitive 4 -> Begin describing “triangle” primitive
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |  |  |  |  | type |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 76: ENDPRIMITIVE instruction
Assembly Formats
  endprimitive
Encoded to
Operation
Description
  Delimit the vertices that define a primitive or a group of primitives.
Examples
  endprimitive
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 77: LOADIDENTITY instruction
Assembly Formats
  loadidentity
Encoded to
Operation
Description
  Replace the current matrix with the identity matrix.
Examples
  loadidentity
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 78: FLUSH instruction
Assembly Formats
  flush
Encoded to
Operation
Description
  Flush (Empty) the contents of the frame buffer.
Examples
  flush
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 79: DRAW instruction
Assembly Formats
  draw
Encoded to
Operation
Description
  Draw the contents of the frame buffer on a screen (if available).
  Also, this instruction indicates the end of frame.
Examples
  draw
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 |  |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 80: Translation, Rotation, Scale Operations
Design options: (1) Set up matrix elements, (2) set up angle
Scaling, Rotation
Transcendental functions
  Use a look-up table ( case statements)
x1’ cosΘ sinθ 0 0
y1’ = -sinθ cosθ 0 0
z1’ 0 0 1 0
1 0 0 0 1
]
[
[
]
x1
y1
z1
1
x1’ Sx 0 0 0
y1’ = 0 Sy 0 0
z1’ 0 0 Sz 0
1 0 0 0 1
]
[
x1
y1
z1
1
[
]

## Slide 81: Matrix Multiplication
OK, we want to do [4x4] [4x1] matrix multiplication. How many multiplier?
  (4*4)*4 = 64 multiplier
  32-bit 64 multiplier
  How many Logic Elements?
Parallel computations? Serial computations? Special functional units for each operation?
x1’ Sx 0 0 0
y1’ = 0 Sy 0 0
z1’ 0 0 Sz 0
1 0 0 0 1
]
[
x1
y1
z1
1
[
]
 x1’=Sx X1, y1’ = Sy Y1, z1’ = Sz Z1

## Slide 82: View Transformation

## Slide 83: GEOMETRY Summary (Review)
model space
world space
world space
compute lighting
camera space
projection
image space
clip
map to screen

## Slide 84: Vertex & Primitives
V1
V2
V3
V1 = (x1, y1, z1)
V2 = (x2, y2, z2)
V3 = (x3, y3, z3)
+x
+y
+z
Normal vectors:
Surface Normals: Physical meaning
Vertex Normals: Useful for fast and effective lighting algorithms

## Slide 85: Primitive Assembly

## Slide 86
Model Space: Each model has own coordinate
Word Space: All models have the same coordinate
Camera Space (Eye Space): Relative to the camera (eye) position. (Camera position, z = 0)
Screen space: Actual hardware coordinates

## Slide 87: Transformation Pipeline
World Transformation
  Model coordinates  World coordinates
View Transformation
  World coordinates  Camera Space
Projection Transformation
  Camera Space  View Plane
Matrix Multiplications for transformations
From Hsien-Hsin Lee’s MPG class

## Slide 88: Homogeneous Coordinates
Adding one more imaginary coordinate
Enable all transformations to be done by “multiplication”
“projective transformations” can be easily represented
Add one coordinate (w) to 3D vector
  W=1 is a cartesian coordinate
  W >1 useful for projective projection

## Slide 89: Transformations
+x
+y
+z
(tx, ty, tz)
+x
+y
+z
(x1’, y1’, z1’)
(x1, y1, z1)
x1’
y1’ =
z1’
[
x1 tx
Y1 + ty
z1 tz
]
[
]
x1’ 1 0 0 tx
y1’ = 0 1 0 ty
z1’ 0 0 1 tx
1 0 0 0 1
]
[
x1
y1
z1
1
[
]

## Slide 90: Others
Scaling
Rotation (with Z-axis)
x1’ Sx 0 0 0
y1’ = 0 Sy 0 0
z1’ 0 0 Sz 0
1 0 0 0 1
]
[
x1
y1
z1
1
[
]
x1’ cosΘ sinθ 0 0
y1’ = -sinθ cosθ 0 0
z1’ 0 0 1 0
1 0 0 0 1
]
[
[
]
x1
y1
z1
1

## Slide 91: Exercise
Write an affine transformation matrix and write down the new coordinates of A, B. The yellowjacket becomes 2 times bigger, 90 rotation (counter clock wise) and move + 1 x-axis
(0,0,0)
(-1,-1,0)
(1,1,0)
(0,0)
A
(0,1,0)
B
A’
B’
(0, -2, 0,0)
(2, 0, 0,0)
(0, 0, 1,0)
(0, 0, 0,1)
A’ = (-1,2,0)
B’ = (3,-2,0)
x1’ Sx 0 0 0
y1’ = 0 Sy 0 0
z1’ 0 0 Sz 0
1 0 0 0 1
]
[
x1
y1
z1
1
[
]
x1’ cosΘ sinθ 0 0
y1’ = -sinθ cosθ 0 0
z1’ 0 0 1 0
1 0 0 0 1
]
[
[
]
x1
y1
z1
1

## Slide 92: Non-commutative Property
[X’] = [A][B][X] ≠ [B][A][X]
+z
+z
Scale by 2
X,Y translate +5, +5
+z
X,Y translate +5, +5
Scale by 2
(1,1,-1)

## Slide 93: Affine Transformation
Line  Line
  keep straight lines, ratios of distances between points
Angle can be changed

## Slide 94: Projects
Orthographic projection
Projective projection

## Slide 95: Canonical View Volume
Orthographic Project
OpenGL GL_Projection matrix
+z
+x
+y
+z
+x
+y

## Slide 96: Field of View
d
ys
y
z
Frustrum: the region of space in the modeled world that may appear on the screen
near
far

## Slide 97: Prospective Projection
near
far
+z
+x
+y

## Slide 98: Data Structures in Pipeline
Vertex assembly
Primitive assembly
Rasterization
Fragment operations
Display
Vertex operations
Application
Primitive operations
struct { float x,y,z,w; float r,g,b,a; } vertex;
struct { vertex v0,v1,v2 } triangle;
struct { short int x,y; float depth; float r,g,b,a; } fragment;
struct { int depth; byte r,g,b,a; } pixel;
Frame buffer
Screen coordinates
Akeley Fall 2007 Slides
Not in this project
Not in this project

## Slide 99: The RASTERIZER stage
From GEOMETRY to visible pixels on screen
Add textures and various other per-pixel operations
And visibility is resolved here: sorts the primitives in the z-direction
Per pixel operation
Mostly integer operations

## Slide 100: How to draw a Line?:Bresenham Algorithm
y = mx + b
Brute-force approach
f(x,y) = (y0-y1)x+(x1-x0)y+x0y1-x1y0=0 (x0<= x1)
When (0<m<=1) , draw (x,y)  draw (x+1,y) or (x+1, y+1)
y = y0
for x=x0 to x1 do
draw (x,y)
if (some condition) then
y = y+1
Condition  f (x+1, y+0.5) < 0 then y = y+1
Shirley’s text book Chapter 3

## Slide 101: Optimization-I
Since f(x,y) = (y0-y1)x+(x1-x0)y+x0y1-x1y0=0
f(x+1, y ) = f(x+y) + (y0-y1)
f(x+1, y+1) = f(x,y) + (y0-y1)+(x1-x0)
We already calculated f(x-1,y+0.5) or f(x-1, y-0.5) after the first iteration
for x=x0 to x1 do
draw (x,y)
if (d <0) then
y = y+1
d = d+(x1-x0)+(y0-y1)
else
d = d+(y0-y1)

## Slide 102: Optimization-II
Remove floating point operations
Use 2f(x,y) instead of f(x,y)
2f(x0+1,y0+0.5) = 2(y0-y1)(x0+1)+(x1-x0)(2y0+1)+2x0y1-2x1y0=0
Resulting code is
y = y0,
d= 2(y0-y1)(x0+1)+(x1-x0)(2y0+1)+2x0y1-2x1y0
for x=x0 to x1 do
draw (x,y)
if (d <0) then
y = y+1
d = d+2(x1-x0)+2(y0-y1)
else
d = d+2(y0-y1)

## Slide 103: Barycentric Coordinates
P
v0
v1
v2
P = aV0+bV1+cV2
a+b+c = 1
P is inside triangle if
0<a<1
0<b<1
0<c<1
a = f12(x,y)/f12(x0,y0)
b = f20(x,y)/f20(x1,y1)
c = f01(x,y)/ f01(x2,y2)
fi,j is the previous function with appropriate vertices

## Slide 104: Gouraud interpolation
Gouraud shaded
  v0, v1, v2 have colors c0, c1, c2
  Color at (x,y) : c = a c0 +b c1 + d c2
  If p is inside the triangle
  Draw c

## Slide 105: Triangle rasterization examples
Gouraud shaded (GTX)
Edge walk, planar parameterization (VGX)
Barycentric direct evaluation (InfiniteReality)
Small tiles (Bali – proposed)
Per-pixel evaluation (Pixel Planes 4)
Akeley’s slides